## Slide 1: Using Multiple Frustums for Massive Worlds
Patrick Cozzi, @pjcozzi
Analytical Graphics, Inc.
University of Pennsylvania
(Slides: cesium.agi.com/massiveworlds)
Notes: I’m a developer at AGI where I develop OpenGL and WebGL virtual globes for aerospace and defense communities.

## Slide 2: Our Work at AGI
High-resolution terrain and sub-meter imagery
Notes: We have some pretty unique requirements in that we model the real-world down to ground stations surrounded by high-resolution terrain and sub-meter imagery. For example, a user can zoom in a see an individual car or even finer-detail.

## Slide 3: Our Work at AGI
Satellites at 40,000 km
Notes: And in the same scene, we can model satellites in high-earth orbit at 40,000 km above Earth…

## Slide 4: Our Work at AGI
Interplanetary missions
Notes: …and also in the same scene, we can model interplanetary missions to the moon or mars.

## Slide 5: Our Work at AGI
Massive view distances and precision for coordinate systems
Notes: The massive scale alone isn’t necessary a problem, but the fact that we need massive-scale with fine-grained detail makes things challenging. For example, a user may want to zoom in close to a satellite and see the sun in the distance since it is important that the satellite’s solar panels are pointed towards the sun. Likewise, we may zoom in close to a satellite and want to be able to see the ground station on Earth that we are maintaining a communication like with.

## Slide 6: Introduction
Massive scale with fine-grained detail
  Precision problems rendering artifacts
Issues
  Earth-scale at meter resolution – jittering
  Global terrain – z-fighting
Notes: It’s when we have massive scale worlds with fine-grained detail that precision problems manifest themselves as rendering artifacts.
In our experience, we run into two main artifacts. The first is jitter. When we have the need for large world coordinates, like when modeling the earth at a meter-scale, floating-point round-off errors in 32-bit vertex transform manifest themselves as bouncing or jittering when we zoom in close.
The other, more well-known issue we run into is z-fighting. It’s pretty common to see on a forum something like “I wrote a terrain engine for a small area and it worked great, but now I’m scaling it up to cover the entire Earth and I’m getting flickering artifacts. Why?”

## Slide 7: Introduction
Robust multiple frustum solution for z-fighting
  No fog
  No bribing artists
Useful for
  Virtual globes
  Geospatial visualization
  Massive-world games
Pragmatic implementation tips
Notes: Today, we’ll intuitively explain why we get z-fighting in massive worlds and look at a robust solution utilizing multiple view frustums that makes very few assumptions. For example:
As we’ll see, adding fog in the distance is a classic trick to help z-fighting, but we won’t require it.
We also can’t ask artists to design a scene such that the maximum view distance is only so far, e.g., add walls. In fact, I don’t even have access to artists. Our end users at the “artists” to some extend, and they design the scene with whatever satellites or anything else they want to put in that isn’t known until runtime.
This technique is not original, but I’m not aware of any really good implementation guides. The concept is easy, but the implementation requires some care so this talk aims to provide guidance.

## Slide 8: Introduction
Huge far-to-near ratio. No Fog!
Notes: Here’s an example of why a classic trick like adding fog won’t always cut it for us. Some of our users want to see all the active unclassified satellites in space at the same time and be able to zoom into individual satellites and see the others in the distance.

## Slide 9: Z-Fighting
Shadow UAV mission without z-fighting
Notes: Here we have a Shadow UAV flying a mission through the mountains.
There are no z-fighting artifacts in this image because the app already accounts for them, but if we naively use the near and far plane distances required for this scene, we see z-fighting artifacts like these…

## Slide 10: Z-Fighting
Close near plane and distant far plane
video
Notes: There is z-fighting throughout the distant mountains. I circled a few of the major areas. Terrain geometry is z-fighting with skirts used to prevent cracks.
Z-fighting is even more irritating when things are moving as shown in the video [videos/zfighting.wmv]. I promise that our software doesn’t do this by default; I hacked it to make the video.
Notice how there is no z-fighting closer to the viewer, for example, with the UAV or nearby foothills.

## Slide 11: Z-Fighting Causes
Coplanar geometry
  Reauthor, polygonOffset, or stencil
“Far apart” geometry can z-fight due to the non-linear relationship between zeye and zwindow
  zeye and zwindow relationship is controlled by the f/n ratio
  Bigger f/n: greater nonlinearity
Notes: Now let’s take a closer look at z-fighting in massive worlds and solutions.
The classic z-fighting example is a piece of paper on a desk. If the paper and the desk are coplanar, we can see z-fighting artifacts due to floating-point round-off error. This particular case can be solved many ways including:
Slightly adjusting the geometry, either when authoring or in a view-dependent way at runtime with a call like polygonOffset [1]
Stenciling. Stencil out the paper. Render the desk. Render the paper.
However, z-fighting can occur when geometry is not coplanar, even when geometry is far apart – in some sense. This is due to the non-linear relationship between z in eye coordinates and z in window coordinates when using a perspective projection.
This relationship is controlled by the far-to-near ratio; a bigger ratio makes the relationship more non-linear. That is, the bigger the view distances and the closer the near plane, the more likely geometry is to z-fight.
[1] http://www.opengl.org/archives/resources/faq/technical/polygonoffset.htm

## Slide 12: Z-Fighting Causes
zwindow is proportional to 1/zeye
Image courtesy http://www.virtualglobebook.com
Due to perspective division
Notes: Let’s look at a few graphs to gain some intuition about this behavior.
When using a perspective projection, if we multiply out the model-view-projection matrix, perspective, divide, and viewport transform, we see that z-window is proportional to 1/z-eye.
Z-window = ((((f + n) / (f – n)) + (2fn / z-eye(f – n))) + 1) / 2
(in the common case when the depth range near is zero and far is one).
For a given perspective projection, everything on the right-hand side is constant except for z-eye, therefore z-window is proportional to 1/z-eye.
This is the result of the perspective divide, which causes perspective foreshortening, making objects in the distance appear smaller.
As we can see in the graph, a small change in z-eye when z-eye is small results in a big change in 1/z-eye because 1/z-eye is a quickly moving function here. That same change in z-eye when z-eye is large results in a smaller change to 1/z-eye because 1/z-eye is slowly moving then. In the later case, a small change to z-eye may yield the same z-window, creating rendering artifacts.

## Slide 13: Z-Fighting Causes
Relationship between zwindow and zeye depends on n and f
Image courtesy http://www.virtualglobebook.com
Notes: The relationship between z-window and z-eye also depends on the near and far distances as shown in this graph.
The x-axis is the distance from the near plane in eye coordinates, from 0 to 100. The y-axis shows z-window from 0 to 1. In all cases the view distance (f – n) is 100. Here we see that as n gets smaller, and hence the far-to-near ratio gets bigger, the precision gets pushed to the near plane.

## Slide 14: Z-Fighting Causes
Minimum Triangle Separation
Image courtesy http://www.virtualglobebook.com
Notes: The minimum triangle separation, s-min, for a distance from the eye, z-eye, is the minimum world-space separation between two triangles required for correct depth occlusion.
[Baker99] provides an approximation to s-min for an x-bit fixed-point depth buffer:
S-min = (z-eye * z-eye) / ((2^x)n – z-eye)
[Akeley06] also show that window coordinate precision, field of view, and error accumulated by single-precision projection, viewport, and rasterization arithmetic contribute to effective depth buffer resolution.

## Slide 15: Z-Fighting Causes
24-bit fixed-point depth buffer
  f/n of 1,000 is acceptable [Akeley90]
Earth semiminor axis is over 6,300,000 meters
  Want fine-grained detail
Notes: A ratio of 1,000 is commonly considered acceptable for a 24-bit fixed-point depth buffer [Akeley90]. In practice, we’ve gotten away with higher values depending on how far apart geometry is. However, 1,000 or even 10,000 is not going to cut it for our massive worlds where Earth’s semiminor axis alone is over 6,300,000 meters.

## Slide 16: Z-Fighting Solutions
Far-to-near tuning
Remove distant objects / imposters
Complementary depth buffering [Persson09, Kemen12]
Logarithmic depth buffer [Kemen08, Ulrich11, Kemen12]
Multiple frustums
Notes: There are a lot of solutions to z-fighting. For some apps, it is possible to just push out the near plane far enough to preserve a reasonable far-to-near ratio for the desired view distance.
This can be combined with removing distant objects, which are likely to z-fighting with themselves or other geometry. Fog can be used so the object is not removed until is is completely covered by fog or alpha blending can be used to fade the object out.
In many cases, distant objects are more likely to z-fight with themselves than to z-fight with other objects, so replacing them with an imposter can help.
Complementary depth buffering or reverse floating-point depth buffering has also been used with good success. It is used in Just Cause 2. Instead of using a 24-bit fixed-point depth buffer, a 32-bit floating-point depth buffer is used. The near and far planes are reversed and so is the depth test. The idea is that the non-linear distribution of z values is somewhat canceled out by the non-linear distribution of floating-point values.
The logarithmic depth buffer has also been used with success. It is used in Outerra. Here a logarithmic distribution of z values is used by either modifying the z value in the vertex shader or the depth value in the fragment shader. When using the vertex shader, long-thin triangles going behind the viewer can cause artifacts and when using the fragment shader, early-z is generally disabled.
Code: https://github.com/virtualglobebook/OpenGlobe (see Chapter06DepthBufferPrecision)

## Slide 17: Multiple Frustums
Multiple frustums
  Virtually unlimited view distances
  Works for WebGL; no EXT_frag_depth
  Works on old hardware
  Easy concept. Implementation requires some care
Notes: The technique I’ll discuss tonight is to simply partition the scene into multiple frustums, each with a sane far-to-near ratio. At AGI, we’ve been doing this for a long time. The story goes – now I was just starting high school at the time – that in the mid 90s when we first started doing 3D we called SGI about our z-fighting issues and they basically said “don’t do that; use a far-to-near ratio of 1,000.” So one of our developers, Ed Mackey, decided to use multiple frustums to keep this ratio.
Other folks have also come up with the same solution as I’ve seen in mentioned on the forum from time to time.
This allows for basically unlimited view distances since we can always add frustums, and also works for WebGL where we currently can’t write depth (however, a draft extension has been proposed). It even works on fixed-function hardware, but hopefully you don’t have to deal with that.
What I hope you find interesting about this talk is that multiple frustums is really simple in concept, but the devil is in the details so to speak. It’s kind of like shadow maps, which sound simple on the surface, but the complexity starts to unfold to handle under-sampling, soft shadows, etc.

## Slide 18: Multiple Frustums
Same fov and aspect ratio
Farther the near plane, the bigger the frustum
A few frustums can cover a large view distance
  Frustum 1: 1 to 1,000
  Frustum 2: 1,000 to 1,000,000
  Frustum 3: 1,000,000 to 1,000,000,000
In practice, we’ll overlap the frustums a bit.
Not to scale
Notes: To use multiple frustums to eliminate z-fighting, each frustum has the same field-of-view and aspect ratio, but different near and far values. Each frustum has a far-to-near ratio of 1,000 or whatever you’d like to set it to. For example, the first frustum may go from 1 to 1,000 meters, and then the next frustum would go from 1,000 to 1,000,000 meters. So it only takes a few frustums to cover a long view distances.
Using multiple frustums for z-fighting is similar to z-partitioning in cascaded shadow maps with the light source directly behind the viewer. Like shadow maps, we’ll want to compute the farthest possible distance for the near plane (light frustum in shadow maps). Cascaded shadow maps improve shadow map under-sampling where as we are using multiple frustums to overcome the distribution of z values.

## Slide 19: Multiple Frustums
Simple implementation
foreach frustum in back-to-front order
{
set projection matrix;
clear depth;
find objects that overlap frustum;
render objects;
}
Not to scale
Notes: Given these frustums, the implementation is simple. We render the scene with a hybrid painter’s algorithm and depth buffering.
We walk the frustums from back-to-front, and set the projection matrix to be for the current frustums. We then clear the depth buffer. This clear is important since when we get to a closer frustum, we want objects that frustum to win the depth test against objects in the previous frustum. After clearing depth, we find objects that overlap the frustum and render them.
A common case for us may be 3 frustums and 300 objects. Each object is frustum culled 3 times, but if most objects are only in one frustum this is wasteful.

## Slide 20: Multiple Frustums in Cesium
Performance goals
  Use the fewest frustums possible
    Dynamic near/far plane
  Minimize objects overlapping multiple frustums
    Push out near plane
  Minimize CPU overhead
    Minimize frustum checks
    Exploit temporal coherence
Notes: Given that most objects will only overlap a single frustum, this can be more efficient. Let’s aim to:
Use the fewest frustums possible based on the needs of the current view, not a fixed near and far plane
Minimize the number of objects overlapping more than one frustum (by pushing out the near plane – and having a larger initial frustum)
Minimize CPU overhead
A spatial data structure can help, but sometimes we don’t want one for dynamic data and there usually isn’t a one-size fits all data structure, e.g., we use a custom one for terrain, nothing for orbit lines, etc.
Here’s I’ll go through the implementation in Cesium, a open-source virtual globe engine that we started.

## Slide 21: Multiple Frustum Rendering in Cesium
1) The scene produces commands that encapsulate draw calls
Render state
Framebuffer
Shader
Vertex array
Bounding volume
Command
Commands come from the terrain engine, 3D models, billboards, polylines, etc.
Notes: The scene produces commands for the renderer to execute. In other literature, a command is also called a “draw call” or a “batch.” Commands may come from the terrain engine or other entitles like 3D models, billboards, or polylines.
A command has everything needed to execute a draw call using the underlying graphics API – WebGL in our case. Our engine has both DrawCommands for issuing drawElements/drawArrays calls and ClearCommands for clearing the framebuffer. Here, we’re just concerned with DrawCommands, which have:
Vertex array, offset, and count
Shader program and its uniforms, including a model matrix
Render state that defines the fixed-function state of the pipeline
Framebuffer, which is the target of the draw call
Strictly speaking, the bounding volume is not used for issuing the draw call, but it is needed for determining what frustums a command belongs to. Any bounding volume could work, but we use spheres everywhere for now.
Code: https://github.com/AnalyticalGraphicsInc/cesium/blob/b16/Source/Renderer/DrawCommand.js

## Slide 22: Multiple Frustum Rendering in Cesium
2) Walk through commands
Cull1
Compute
  Min near distance
  Max far distance
Application distances define extremes
1If it wasn’t already; the scene culls some commands hierarchically
Min near
Max far
App near
App far
Notes: The near and far plane distances can varying frame-to-frame. The farther we can push out the near plane and the closer we can bring in the far the plane, the fewer frustums we will have. So instead of just using the application-defined near and far distances, we compute them dynamically using each command’s bounding volume and the application-defined distances as extremes.
In our engine, we do both frustum culling and horizon culling, which is occlusion culling with the ellipsoid, as Kevin will discuss in the following talk.
We don’t need to check the far plane in this cull pass.
Code: createPotentiallyVisibleSet() in https://github.com/AnalyticalGraphicsInc/cesium/blob/b16/Source/Scene/Scene.js

## Slide 23: Multiple Frustum Rendering in Cesium
3) Given desired far-to-near ratio, determine the number of frustums
var numFrustums = Math.ceil(
Math.log(far / near) / Math.log(farToNearRatio));
for (var m = 0; m < numFrustums; ++m) {
var n = Math.max(near, Math.pow(farToNearRatio, m) * near);
var f = Math.min(far, farToNearRatio * n);
// ...
Notes: Code: updateFrustums() in https://github.com/AnalyticalGraphicsInc/cesium/blob/b16/Source/Scene/Scene.js

## Slide 24: Multiple Frustum Rendering
4) Walk through commands, and assign them to frustum(s)
Can combine with Step 2 in a single pass over the commands by exploiting temporal coherence – using the frustums computed from the previous frame
Notes: Now that we know the length of each frustum, we can walk through the commands again, and assign to them frustums that they overlap. As we’ll see some commands will wind up in more than one frustum.
So far, the renderer has made two passes over commands – the first pass culls and computes the frustums, and the second pass assigns commands to frustums. A typically application will have 100s to 1,000s of commands so it would be nice to be able to do this in a single pass. We can by exploiting temporal coherence.

## Slide 25: Multiple Frustum Rendering
4) Temporal Coherence Criteria
neart >= near(t – 1)
fart <= far(t – 1)
numFrustumst == numFrustums(t – 1)
near(t – 1)
far(t – 1)
fart
neart
Notes: It is very likely that the frustums computed in the previous frame can be used in the current frame. We define our acceptance criteria as:
desired near >= previous near
desired far <= previous far
desired number of frustums == previous number of frustums
Code: createPotentiallyVisibleSet() and insertIntoBin() in https://github.com/AnalyticalGraphicsInc/cesium/blob/b16/Source/Scene/Scene.js

## Slide 26: Multiple Frustum Rendering in Cesium
Good coherence using
application-defined near distance
Poor coherence when zooming in
Notes: Coherence can be really good, especially when the user-defined near distance is used because the closest bounding volume intersects it because, for example, the viewer is deep in the mountains or following a satellite as shown here. This is a lot of our use cases.
Coherence is not so good in other cases, like, when zooming in to an object because the desired near distance keeps getting smaller and smaller.
We could improve coherence by scaling the computed near/far to be slightly farther apart, but this runs the risk of requiring new frustums.

## Slide 27: Multiple Frustum Rendering in Cesium
2-4) Walk through commands
Frustum cull
Assign commands to previous frame frustums
Compute desired near/far distance
Compute new frustums and repeat if new frustums are needed
Notes: So Steps 2-4 are really combined into a single pass over the commands. We cull a command as before, then assign it to frustum(s) using the previous frame’s frustum. As we walk through each command, we still compute the desired near/far distances. Then we use these to determine if the previous frame’s frustums will work. If they won’t we compute new frustums, and call the function again knowing that the computed frustum will work.

## Slide 28: Multiple Frustum Rendering in Cesium
Render like we did before
foreach frustum in back-to-front order
{
set projection matrix;
clear depth;
render commands overlapping this frustum;
}
Notes: Now we know the tight near/far distances and the commands in each frustum

## Slide 29: Multiple Frustum Artifacts
Artifacts without frustum overlap
video
Notes: If adjacent frustums do not overlap slightly, we’ll see tearing artifacts where the near plane of one frustum meets the far plane of the closer frustum. In the lower image here, we see several tears revealing the background color where two frustums meet.
When we first saw this artifact, we thought it was a driver bug, but we saw it across hardware vendors. With the near plane of a frustum equal to the far plane of the closer frustum, I can imagine one pixel artifacts, but these artifacts are much larger.
To solve these, we move the near plane of each frustum, except the closest, slightly closer.
Code: updateFrustums() in https://github.com/AnalyticalGraphicsInc/cesium/blob/b16/Source/Scene/Scene.js
Video: videos/frustumOverlap.wmv

## Slide 30: Multiple Frustum Artifacts
Artifacts with frustum overlap
video
Notes: Overlapping frustums creates a new artifact for objects rendered with blending. In our engine, we render a lot of large translucent objects for polygons or to represent sensors, e.g., a view volume of a camera attached to a satellite. Since these objects are large, they often overlap more than one frustum. Since they use alpha blending for translucency, the blending occurs twice where the frustums overlap leading to artifacts that can appear to slide back and forth when the viewer zooms.
I am experimenting with stenciling to eliminate these artifacts, but the results so far only work in limited cases. The idea is to write the current frustum’s zero-based index (counting from the farthest frustum) to the stencil buffer and only pass the stencil test if the fragment was not written in previous frustums as indicated by the stencil value.

## Slide 31: Performance: Redundant Draw Calls
1 Frustum. 14 Commands
Notes: When a bounding volume overlaps more than one frustum, not only does it have the potential to create artifacts, but it leads to commands being executed redundantly, that is, executing draw calls for the same object in more than one frustum. How, it’s actually not as bad as you’d think. Let’s look at a few different scenes.
For this full world view, we execute 14 commands (ignoring clears, the sky box, and 2D overlays). They all fit within one frustum because we are able to dynamically push the near plane back really far, which allows the first frustum to be large enough to include the entire globe.

## Slide 32: Debug View
Frustum 1 - red
Frustum 2 - green
Frustum 3 – blue
1 + 2 – yellow
2 + 3 - cyan
1 + 2 + 3 - white
Notes: This view is useful to visualize where frustum boundaries are (which move with the camera) and to see how many commands are in more than one frustum like the yellow above.

## Slide 33: Performance: Redundant Draw Calls
2 Frustums. 109 Commands. 21 executed twice
Notes: Here we are zoomed in much closer to the ground looking at Mount Everest. For this scene, we execute 109 commands (horizon views are always a challenge; note there is no fog here allowing us to not draw distant tiles). 21 are executed twice.

## Slide 34: Performance: Redundant Draw Calls
2 Frustums. 83 Commands. 2 executed twice (not visible)
Notes: Not all horizon views are that bad. Here we are looking at Mount Everest. Out of the 83 commands, only 2 are executed twice. Those 2 pass view frustum culling but don’t actually result in any pixels.

## Slide 35: Performance: Redundant Draw Calls
3 Frustums. 6 Commands. 2 executed three times
Notes: We’re not always this lucky with redundant calls. For example, we are high in space in this scene. We need three frustums total.
This scene only needs six commands, but two of them execute in all three frustums. Can you guess which? The billboards for the satellites are batched together as are the labels for the satellites. Since the bounding sphere for these includes the Molniya orbit high in space and right in front of the viewer – which peaks at 40,000 km above the globe, and the Geoeye in low earth orbit. This creates a huge bounding volume that overlaps all three frustums.

## Slide 36: Performance: Batching vs. Culling
Bigger batch
Bigger bounding volume
More likely to overlap multiple frustums
Need tight bounding volumes, e.g., [Ohlarik08b]
Bounding volumes for dynamic objects
We still prefer to aggressively batch
Notes: Everything needs to have a bounding volume. For something dynamic like a particle system, the bounding volume doesn’t have to be recomputed every frame, it can encompass the particles expected position over their lifetime.
This shows that there is tension between batching and culling even more so when using multiple frustums. Traditionally, to make the best use of the GPU, and minimize CPU overhead, we always try to reduce the number of draw calls we make during a frame by batching. When we introduce multiple frustum rendering, batching generally increases bounding volume sizes, making it more likely that a command (batch) will need to be executed in more than one frustum, which increases the number of draw calls. Given that applications built on our engine are almost always CPU bound, we still see a win by batching aggressive even if it leads to some redundant draw calls.

## Slide 37: Performance: Fill Rate
Need several depth clears; may need to clear depth separate from stencil
More overdraw less opportunities for Hi-Z and Z-Cull
  Can only sort/pre-pass within a frustum
  Can’t render the sky box last
    Unless it is rendered in every frustum
Notes: At the end of the frame, only the depth values for the closest frustum are in the depth buffer so we can’t render the sky box last to take advantage of early-z. Instead, we rendering the sky box first, without reading/writing depth, using the projection matrix for the entire frustum.

## Slide 38: Future Ideas
Size frustums to minimize command overlap
  Similar to kd-tree splitting plane
  Minimize overlap and maintain far-to-near ratio
  Use application CPU time in hopes of less draw calls
Better temporal coherence
Artifact-free frustum overlap
Notes: Another idea (probably with diminishing returns): better temporal coherence (like loose octrees).

## Slide 39: Advice
Only use multiple frustums if the app really needs it
  Try complementary or logarithmic depth buffer first

## Slide 40: Acknowledgements
Ed Mackey, @emackey
Dan Bagnell
Deron Ohlarik
Notes: Ed did our original multi-frustum implementation in the late 90s. Dan did most of the recent implementation work in Cesium, our WebGL engine.

## Slide 41: References
[Akeley90] Kurt Akeley. The Hidden Charms of the z-Buffer. IRIS Universe, 1990.
[Akeley06] Kurt Akeley and Jonathan Su. Minimum Triangle Separation for Correct z-Buffer Occlusion. Graphics Hardware, 2006
[Baker99] Steve Baker. Learning to Love Your z-Buffer. 1999
[Cozzi11] Patrick Cozzi and Kevin Ring. 3D Engine Design for Virtual Globes. A K Peters, Ltd., 2011
[Kemen08] Brano Kemen. Logarithmic Depth Buffer. 2008
[Kemen12] Brano Kemen. Maximizing Depth Buffer Range and Precision. 2012
[Ohlarik08a] Deron Ohlarik. Precisions, Precisions. 2008
[Ohlarik08b] Deron Ohlarik. Bounding Sphere. 2008
[Persson09] Emil Persson. A Couple of Notes about Z. 2009
[Ulrich11] Thatcher Ulrich. Logarithmic Depth Buffer. 2011
Notes: In addition to these references, also see the implementation notes with pseudo-code for our engine - https://github.com/AnalyticalGraphicsInc/cesium/wiki/Data-Driven-Renderer-Details

## Slide 42: Course Resources
cesium.agi.com/massiveworlds

## Slide 43
Bonus Slides
(slides that didn’t make the cut due to time constraints)

## Slide 44: Jitter
Landsat 7. 700,000 m above Earth. Inertial reference frame.
video
State border. WGS84 reference frame.
See [Ohlarik08b]
Notes: The other artifact we’re going to look at today is jitter.
Here we have the Landsat 7, which is an imaging satellite in orbit at about 700,000 m above Earth. The billboard and text have the same world position. However, a small change in the viewer position results in the white polyline representing the satellite’s orbit, to bounce – or jitter..
Like z-fighting, jittering is most noticeable and irritating when things are moving. In this video [videos/jitter.wmv], we see a red polyline that looks innocent enough. As we zoom in and rotate, it starts to bounce around. This polyline represents the boundary for Pennsylvania, and it is defined in WGS84, which is a coordinate system that has an origin at the center of the Earth. Now we zoom out and see the Landsat 7 satellite again. With the video it is easy to see the polyline bounce up and down.
For this video, I modified our engine to show jitter for the polyline, but not for the billboard and text.